## Slide 1
Automatically Tuning ICF Shock Ignition Targets
Matt Terry and Joseph Koning
Lawrence Livermore National Laboratory
This work was performed under the auspices of the U.S. Department of Energy by
Lawrence Livermore National Laboratory under Contract DE-AC52-07NA27344.
Lawrence Livermore National Laboratory, P.O. Box 808, Livermore, CA 94551
Python for Scientific Computing Conference
Austin, Texas
June 1, 2011

## Slide 2: ICF works by compressing DT fuel to high density and relying on the fuel inertial to confine it
A high intensity driver (x-rays, laser, heavy ion beam, etc) illuminates the surface of a layered spherical pellet
The outer surface of the pellet ablates, compressing DT fuel and driving an imploding spherical rocket
The dense imploding shell stagnates on axis and converts its kinetic energy to thermal energy
The high stagnation temperature initiations a fusion burn wave. The burn wave propagates faster than the shell can disassemble, releasing large amounts of energy
http://en.wikipedia.org/wiki/File:Inertial_confinement_fusion.svg

## Slide 3: Implosion Movie Coming

## Slide 5
Pre-pulse

## Slide 6
Main Pulse

## Slide 7
Igniter Pulse

## Slide 8: Build a tuned pulse by appending optimized the pieces
Pulse start times and powers must be adjusted to have the correct behavior
Adjusting (“tuning”) by hand has high latency and is labor intensive
We can construct objective functions that implement the “eye balling” heuristics that people use when manually tuning
Construct a tuned pulse by appending tuned pieces
tuners = [shock_sync, shock_sync, shock_sync, max_rhor, max_yield]
segments = [‘shock2’, ‘shock3’, ‘shock4’, ‘main’, ‘ignite’]
laser = Laser()
for tuner, seg in zip(tuners, segments):
tune_val = tuner(deck, laser, seg)
setattr(laser, seg, tune_val)

## Slide 9
Python Controller
Tuning Strategy
Input file generation
Numerical Optimization
HYDRA
Hydrodynamics
Radiation Transport
Embedded Python
Shock Tracking
ρR monitors
Output frequency control
Fork
Join

## Slide 10: Python is both extended by and embedded in Hydra
Python is extended through a module called “hydra” which contains functions and objects to manipulate hydra data structures
Python is then embedded in the hydra executable
Bottom line: Hydra makes available a Python interpreter running concurrently in parallel with the main Hydra executable. The two processes are loosely coupled through the “hydra” Python module

## Slide 11: Interesting lessons learned
Propagating modifications to the parser is tricky
  Need a custom parser
  from __future__ import with_statement
Saving the state of __main__ across restarts is tricky
  Cobble together many methods to collect state
  Pickle state as a string and add it to restart files
  Some objects pickle but do not unpickle!
If your program uses different indexing than Python, resist the urge to emulate your program’s indexing in Python

## Slide 12: Auto-tuner needs to generate, run and process many simultions
Input file generators that wrap a “template” input file
  Modify simple Hydra variable assignments
  Delegate complicated input file structures to special purpose objects
  Inject commands into the input file by overwritings sentinels with str(python_proxy_of_complicated_thing)
Output file wrappers extract data from Hydra binary output files
Embedded diagnostics using embedded Python interpreter
  Characteristic (shock) trackers with finish line triggers
  Change graphics dump frequency based on shock locations
  ρR monitors

## Slide 13: Pre-pulse consists of a picket and 3 pedestal segments
Picket launches a 1 MBar shock and acts as a fiducial for synchronizing subsequent shocks
Intensity and shape of picket are set by 2D stability considerations and are assumed as givens for this work (see future work)
Pedestals launch shocks which increase density by ~4x
  Near maximum compression for a planar shock
  Stronger shocks decrease performance by increasing entropy (drop compressibility)
Maximum fuel compressibility is very important so shocks should coalesce outside of fuel

## Slide 14: Lets focus on the pre-pulse shocks

## Slide 15: Each pulse segment launches shock which can be unambiguously identified and tracked
Picket Shock
Second Shock
Third Shock
Fourth Shock
Radius (cm)
Time (μs)
Incident Laser Power (TW)
20
15
10
5
0

## Slide 16: Each pulse segment launches shock which can be unambiguously identified and tracked
Picket Shock
Second Shock
Third Shock
Fourth Shock
Radius (cm)
Time (μs)
Incident Laser Power (TW)
20
15
10
5
0

## Slide 17: To maintain low fuel entropy, pre-pulse shocks should be timed to coalesce at gas/ice interface within 50 ps of each other
“Breakout time” is when the first shock crosses the gas/ice interface
All pre-pulse shocks should coalesce at the gas/ice interface at the same time
Good Timing
Interface
Mis-timing < 50ps

## Slide 18: To maintain low fuel entropy, pre-pulse shocks should be timed to coalesce at gas/ice interface within 50 ps of each other
Bad Timing
Shocks merge before interface
Breakout time for bad timing is earlier than for good timing
Breakout time for shocks launch too early is sooner than ideally launched

## Slide 19: To maintain low fuel entropy, pre-pulse shocks should be timed to coalesce at gas/ice interface within 50 ps of each other
Bad Timing
If the second shock is launched too late, the first shock “wins” and the breakout time is unchanged

## Slide 20: We construct an objective function which is biased to find the earliest launch with the saturated breakout time
A tuned shock is the earliest shock launched that also has the asymptotic breakout time
Experimentally tune ω to ensure good convergence, but introducing minimal error
ω = 10% slope between first & last point works well

## Slide 21: Tuning method demonstrates breakout time unchanged after iteratively tuning of segments of pre-pulse
Foot Shock Start
Third Shock Start
Fourth Shock Start

## Slide 22: Main pulse is tuned to maximize burn fraction by maximizing areal density
Having assembled the fuel to high density with the pre-pulse, the main pulse accelerates the shell to high velocity
The duration of main pulse constrained by energy budget, so the onset of the main pulse must be timed to get the most “effective” acceleration
Largest potential burn fraction is a good definitions of “effective”
Assuming ignition, the fuel burn fraction scales with areal density (ρR) :
Tune main pulse to maximize areal density

## Slide 23: Igniter pulse is tuned to maximize thermonuclear yield
Shell boundary
First Shock
Rebound shocks
Ignition shock
Shock Collision
G. Schurtz X.Ribeyre et al.
Igniter shock should arrive near peak compression
Too early and shock energy is diluted over large hot spot
Too late and hot spot will disassemble before arrival of igniter shock
Robust targets should have an “ignition window” where target burns robustly despite some mistiming
Yield
Igniter Shock Launch Time

## Slide 24: Embedded Python interpreter enables “introspective” programs without major software development effort
Shock tracking and triggers
Dynamically changing dump frequency
Areal density (ρR) monitors and triggers

## Slide 25: Summary
Manually tuning a laser pulse to a specific target is normally a labor intensive, high latency process
Tuning can be automated given a sufficiently unambiguous description of “tuned”
For laser shock ignition targets, the initial picket pulse sets the shock breakout time and other pre-pulse shocks should break out as close to this shock without changing the overall breakout time
Main pulse should maximize areal density as to maximize burn fraction when ignited
Igniter shock should be timed to maximize TN yield
Timing algorithm assumes interaction between different pulse features is primarily hydrodynamic, allowing for tuning method to ignore interaction between features

## Slide 26: Optimizations use a parallel 8-wide direct search method
Function evaluations are relatively expensive (10-20 minutes) so want parallel method that minimizes number of iterations rather than number of function evaluations
8 parallel function evaluations per generation (1 per processor)
Start times equally spaced between end points
If f(xi) is a maximum, refine end points to xi-1 and xi+1
Jobs within a generation have nearly the same run-time, so processor utilization is high
Converging timing error to < 50 ps typically takes 3-4 generations
  ~1 hour wall time
Method is simple to implement and has acceptable convergence rate